## Slide 1: FLOODAWARE An agent-based model for near real-time simulation of flood events Anton Bommel Pascal Perez

## Slide 2
Case Study
NSW
Wollongong LGA
Fairy & Cabbage Tree Creeks catchment

## Slide 3
Smart Waterways project
Notes: SMART at large: funded in 2010 ($60m from Commonwealth, NSW and UOW)
Building completed in 2011, contains 30 teaching and research labs, 150 research staff and 200 postdoctoral students.
Spoke and hub model with at the core the Infrastructure Data & Simulation group: 4 labs, 20 researchers and 10 PhD students.

## Slide 4
Topography
Flood event – August 1998
High Risk Area – Flash Flood

## Slide 5
Traditional modelling approach
Hydraulic model
Runoff-Flood
TUFLOW (WBM, 1989)
Hydrological model
Rainfall-Runoff
WBNM (Boyd, Rigby & VanDrie, 1996)

## Slide 6
With :
A Area of the sub-catchment (in km2)
IMP % of impervious area
Q outflow from the subcatchment (in m³/s)
Lag lag time of the sub-catchment (in hours)
WBNM: semi empirical rainfall-runoff model
I – Q = dS / dt (1)
where I = inflow rate at time t (m3/s)
Q = outflow rate at time t (m3/s)
S = volume of water stored on catchment surface at time t (m3)
t = time (s)
The stored volume is related to the outflow discharge by
S = 60. K. Q (2)
where K = lag time between centroids of inflow and outflow hydrographs (minutes).

## Slide 7
FLOODAWARE: near real-time flood modelling

## Slide 8
FLOODAWARE: hybrid architecture
Cellular Automaton
Functional sub-basins
Agent-based architecture

## Slide 9
FLOODAWARE: on-the-fly validation & re-calibration
Smart sensing network
BOM
radar
5 min
5 min
5 min
WBNM
Rainfield 3
recalibrate
predict
predict
recalibrate
FloodAware

## Slide 10
FLOODAWARE: preliminary results

## Slide 11
FLOODAWARE: preliminary results

## Slide 12
FLOODAWARE: preliminary results

## Slide 13
Conclusion
Preliminary results only!
Focusing on operational rather than planning needs
Moving from predictive to self-correcting flood modelling
Ingesting near real time data from smart sensing network
Using AI-based analytics for fast recalibration

## Slide 14
KEEP IN TOUCH
pascal_perez@uow.edu.au
linkedin.com/company/smart-infrastructure-facility-university-of-wollongong
slideshare.net/smart_facility
@SMART_Facility
smart.uow.edu.au
uowblogs.com/smartinfrastructure
SMART Infrastructure Facility